# A3 Light switching centre control unit

## Connector location views

| Number | X-pin, colour | Description |
| --- | --- | --- |
| X12 | 54-pin, black | Plug connector Light switching centre control unit |

## Pin assignments at plug connector X12

| Pin | Type | Description / Signal type | Connection / Measuring notes |
| --- | --- | --- | --- |
| 1 | A | Signal Rear left direction indicator | Connector Rear left direction indicator |
| 2 | A | Activation, right bi-xenon headlight | Xenon headlight, right |
| 3 | A | Signal, right auxiliary direction indicator light | Front right auxiliary flasher unit |
| 4 |  | Not used |  |
| 5 | A | Signal, left brake light | Tail light, left |
| 6 | E | Terminal 30 | Fuse F106 |
| 7 | A | Signal, left low beam light | Left low beam |
| 8 | A | Signal, right high beam light | Right high beam |
| 9 | A | Interface, lights switching centre, trailer module | Trailer module |
| 10 | A | Signal Right brake light | Connector Right brake light |
| 11 | A | Signal, front right direction indicator | Right front turn signal indicator |
| 12 | A | Signal, left/right direction indicator switch | Turn indicator/low beam switch |
| 13 | A | Signal, high beam/headlight flasher switch | Turn indicator/low beam switch |
| 14 | A | Signal, rear load sensor | Load sensor, headlight vertical aim control |
| 15 | E | Terminal 15 | Fuse F32 |
| 16 | A | Signal, centre brake light | Centre brake light |
| 17 | A | Signal, licence plate light | Licence plate lights |
| 18 | A | Signal, left auxiliary direction indicator light | Front left auxiliary flasher unit |
| 19 | A | Signal ground, front load sensor | Load sensor, headlight vertical aim control |
| 20 |  | Not used |  |
| 21 | E/A | K-bus signal | K-bus connector |
| 22 | A | Signal, front load sensor | Load sensor, headlight vertical aim control |
| 23 | A | Signal, +5 V front load sensor | Load sensor, headlight vertical aim control |
| 24 | A | Signal, hazard warning switch | Hazard warning/central locking switch |
| 25 | E | Brake light | Connector Brake light |
| 26 | A | Signal, +5 V rear load sensor | Load sensor, headlight vertical aim control |
| 27 | E | Terminal R | Fuse F9 |
| 28 | A | Signal, fog light relay activation | Fog light relay |
| 29 | A | Outer right tail light | Connector Outer right tail light |
| 30 | A | Outer left tail light | Connector Outer left tail light |
| 31 | M | Ground | Ground connector |
| 32 | M | Ground | Ground point |
| 33 | E | Terminal 30 | Fuse F107 |
| 34 | A | Signal, right low beam light | Right low beam |
| 35 | A | Signal, left high beam light | Left high beam |
| 36 | A | Activation, left bi-xenon headlight | Xenon headlight, left |
| 37 |  | Not used |  |
| 38 |  | Not used |  |
| 39 | A | Signal, headlight vertical aim control Q22 motor, left | Actuator, headlight vertical aim control, left |
| 40 | A | Signal, headlight vertical aim control Q11 motor, left | Actuator, headlight vertical aim control, left |
| 41 | A | Signal, headlight vertical aim control Q12 motor, left | Actuator, headlight vertical aim control, left |
| 42 | A | Signal, headlight vertical aim control Q21 motor, left | Actuator, headlight vertical aim control, left |
| 43 | A | Signal Rear right direction indicator | Connector Rear right direction indicator |
| 44 | A | Signal, front right parking light | Right parking light |
| 45 | A | Signal, front left parking light | Left parking light |
| 46 | A | Signal ground, rear load sensor | Load sensor, headlight vertical aim control |
| 47 | A | Signal Locator lighting | Connector, instrument and locator lighting |
| 48 | A | Signal, lamp in hazard warning switch | Hazard warning/central locking switch |
| 49 | A | Signal, rear fog light | LHD: Boot lid lamp, left RHD: Boot lid lamp, right |
| 50 | A | Signal, front left direction indicator | Front left turn signal indicator |
| 51 | A | Signal, headlight vertical aim control Q22 motor, right | Actuator, headlight vertical aim control, right |
| 52 | A | Signal, headlight vertical aim control Q11 motor, right | Actuator, headlight vertical aim control, right |
| 53 | A | Signal, headlight vertical aim control Q12 motor, right | Actuator, headlight vertical aim control, right |
| 54 | A | Signal, headlight vertical aim control Q21 motor, right | Actuator, headlight vertical aim control, right |

# Light switch centre (LSZ)

In addition to the electronic control and monitoring system for the external vehicle lights, the light switch centre also comprises the switch for sidelights/dipped beam, the pushbuttons for fog lights and rear fog lights as well as the potentiometers for instrument locator lighting and manual headlight vertical aim control.

## Scope of functions of light switching centre

- Control and monitoring of the outer headlights and lamps, including the indicator and hazard warning flasher function

- Control of relay for fog lights

- Evaluation of load sensors for automatic headlight vertical aim control and the resulting activation of stepper motors of evaluation of potentiometer for manual headlight vertical aim control.

- Dimmer function for instrument and locator lighting (terminal 58g) as well as the function and locator lighting for the hazard warning switch.

Communication with other control units and diagnosis takes place via the K-bus. The light switching centre receives information via this bus relating to the vehicle status and also provides information on the status of the controlled lamps (defective/OK, switched ON/OFF).

The indicator lamps for full beam, fog light, rear fog light and direction indicators in the instrument cluster are controlled by the light switching centre on the basis of K-bus telegrams.

## Design

### The light switch centre consists of a control unit and operating panel

Both units are interconnected by means of a plug connector.

### Control unit

The control electronics is accommodated in the control unit.

### Operating panel

The switches for sidelights/dipped beam, fog lights/rear fog lights as well as the dimmer for headlight vertical aim control and instrument lighting are integrated in the operating panel.

The operating panel can be replaced separately from the control unit.

If replacement is necessary, corresponding reference to this is made in the test module.

## Lamp monitoring

The lamps are monitored in OFF and ON status.

Cold monitoring in the OFF status takes place by briefly switching on the lamp (so short that the lamp does not light up). The lamp current is monitored and an assessment is made as to whether the lamp is defective or not.

Note

If the battery voltage drops below approx. 9.5 V, the lamp status can no longer be monitored or output.

## Activating indicator lamps in the instrument cluster

The indicator lamps for left direction indicator, right direction indicator, rear fog lights, fog lights, full beam as well as the LEDs in the pictogram incorporated in the instrument cluster are activated via the K-bus.

## Emergency mode

Independent hardware is provided in order to maintain the functions necessary for driving safety in the event of the control unit failing.

If the light switching centre is in emergency mode,

- Tail lights and dipped beam lights are switched on at terminal 15 irrespective of the position of the corresponding light switch

- Left and right brake lights are switched on at terminal 15 and the brake light switch operated

- Direction indicators, hazard warning lights, full beam, headlight flasher, fog lights and rear fog lights cannot be switched on.

- Diagnosis is not possible

If in emergency mode, the light switching centre must be replaced.