Q: Just when I thought I had everything all good to go with LED's. I just installed all turn signals with LED bulbs with resistors. Everything seemed fine, no "lights out" indication and no “hyper flash”. One thing I do notice is that all of my turn signals flicks a flash every 30 seconds automatically. Why it does that and what do I need to do to prevent that?

A: It is the signal from the LCM, checking for light bulbs out. Solution is very easy. Use a resistor and capacitor to filter out the pulse.

I have used a 10-ohm resistor and 440uF capacitor to filter pulses in the rear boot lights. Those values should also work on the turn signals. You already have a resistor (probably 6 ohms?), so just get the capacitor and rewire as following:

Resistor         LED

+ Light wire ---------+--^^^^^^--+-------->|----+

|          |              |

+----|(----+              |

+Capacitor-              |

|

- Light wire (brown)____________________________+

For the capacitor, get an electrolytic capacitor at least 16volts (I would get 25 or 50 volts rating to be safe). Maplins or local electronics shops should have it.